## Slide 1: CISC 250 – Business Telecomm Networks
Data Link Layer & Local Area Network

## Slide 2: Outline
LAN protocol architecture
LAN devices
MAC Address and ARP
Ethernet
LAN media access methods

## Slide 3: LAN Protocols: Data Link Layer
Data link layer has responsibility of transferring datagram from one node to adjacent node over a link
Datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link protocol provides different services
Data link layer packet is called frame, encapsulates network layer datagram (e.g. IP packet)
“link”

## Slide 4: LAN Protocols: Frame

## Slide 5: Adaptors Communicating
Data link layer implemented in Network Interface Card (NIC) (aka “adaptor”)
  Ethernet card, PCMCIA card, 802.11 card
sending side:
  encapsulates datagram in a frame
  adds error checking bits, flow control, etc.
receiving side
  looks for errors, flow control, etc
  extracts datagram, passes to rcving node
sending
node
frame
rcving
node
datagram
frame
adapter
adapter
Data link layer protocol

## Slide 6: LAN Devices
Repeater
  Allows signal to travel a longer distance on the media
  Classified as layer 1 (physical layer) device
Hub
  Also known as a multi-port repeater
  Creates central connection point for wiring media
  Classified as layer 1 (physical layer) device

## Slide 7: LAN Devices
Bridge
  Connects two LAN segments to make one larger continuous LAN
  Considered layer 2 (data link Layer) device
Switch
  Sometimes called a multi-port bridge
  Forwards data only to the appropriate port for the intended recipient
  Considered layer 2 (data link Layer) device

## Slide 8: MAC Addresses
Each adapter on LAN has an unique MAC address
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 9: MAC Addresses
MAC address:
  is used to get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs) burned in the adapter ROM
Usually expressed for humans in hexadecimal
  Base 16: Each symbol represents 4 bits (for example, 0101=5 hex)
  Convert each four bits to a hex symbol between 0 and F
  Put dashes between each pair
  Example: A1-34-CD-7B-DF-89

## Slide 10: MAC Address
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on IP subnet to which node is attached

## Slide 11: IP Address vs. MAC Address

## Slide 12: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
knowing B’s IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 13: ARP protocol: Same LAN
A wants to send datagram to B, but B’s MAC address is not in A’s ARP table.
A broadcasts ARP query frame, containing B's IP address
  Dest MAC address = FF-FF-FF-FF-FF-FF
  all machines on LAN receive ARP query
B receives ARP frame, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 14: LAN Protocols: IEEE 802 Standards
Internet Layer
Media
Access
Control
Layer
Data
Link
Layer
Logical
Link
Control
Layer
TCP/IP Internet Layer
Standards
Other Internet Layer
Standards
802.2
Other MAC
Standards
(802.5,
802.11, etc.)
Ethernet 802.3 MAC Layer
Standards
Physical Layer
10
Base-T
100
Base-TX
1000
Base-TX
Other
Physical
Layer
Standards
(802.5,
802.11, etc.)

## Slide 15: Ethernet – IEEE 802.3
“dominant” wired LAN technology:
  Cheap - $20 for 100Mbs!
  first widely used LAN technology
  Kept up with speed race: 10 Mbps – 10 Gbps
Connection choices: hub or switch
Metcalfe’s Ethernet sketch

## Slide 16: Ethernet Standards: Physical Layer
802.3 10Base-T
  10 Mbps
802.3 100Base-TX
  100 Mbps
802.3 1000Base-T
  Gigabit Ethernet
Physical
Layer
Notes: > Hello can anyone tell me what the X indicates in a TX or FX cable. > It doesn't "stand for" anything. When we were developing the 100 Mb/s Ethernet standard, a proposal was initially presented for an encoding scheme that supported both twisted pair and fiber. To facilitate discussion, it was called "100BASE-X", where the "X" was a placeholder for whatever medium would ultimately be used. The symbolism stuck and we kept the "X" designation to indicate the use of 4B/5B block encoding; -TX meant that coding on twisted pair, and -FX meant that encoding used on fiber.

## Slide 17: UTP (unshielded twisted pair)
Cat 1: Previously used for POTS telephone communications, ISDN and doorbell wiring.
Cat 2: Previously was frequently used on 4 Mbps token ring networks.
Cat 3: used for data networks using frequencies up to 16 MHz. Historically popular for 10 Mbps Ethernet networks.
Cat 4: Provided performance of up to 20 MHz, and was frequently used on 16 Mbps token ring networks.
Cat 5: Provided performance of up to 100 MHz, and was frequently used on 100 Mbps Ethernet networks. May be unsuitable for 1000BASE- T gigabit Ethernet.
Cat 5e: Provides performance of up to 100 MHz, and is frequently used for both 100 Mbps and Gigabit Ethernet networks.
Cat 6: Provides performance of up to 250 MHz, more than double category 5 and 5e.
Cat 6a: Provides performance of up to 500 MHz, double that of category 6. Suitable for 10GBase-T.

## Slide 18: LAN Media Access Methods
Determines how nodes share channel, i.e., determine when node can transmit
  two or more simultaneous transmissions by nodes: interference
    collision if node receives two or more signals at the same time
Two main ways
  CSMA/CD – used in Ethernet (MAC Layer)
    http://www.youtube.com/watch?v=yGJGIUa-xWE
  Token passing

## Slide 19: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Carrier Sense Multiple Access (CSMA)
  If a NIC wishes to transmit, it must listen for traffic
    If there is no traffic, the NIC may transmit
    If there is traffic, the NIC must wait to transmit until no traffic is being transmitted; then it may send

## Slide 20: Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Collision Detection (CD)
  If there is a collision (by two or more stations transmitting at the same time),
    All NICs stop transmitting and wait for a random amount of time
    The first NIC that finishes its wait may transmit
      but only if there is no traffic!
      If there is traffic, the NIC must wait until there is no traffic
  If there are multiple collisions,
    The random wait is increased each time
    After 16 collisions, the sending NIC discards the frame