## Slide 1: CISC 250 – Business Telecomm Networks
Switched LAN

## Slide 2: Today’s Outline
Switched LAN
  Switch Operation
  VLAN

## Slide 3: Switch
Link layer device
  stores and forwards Ethernet frames
  examines frame header and selectively forwards frame based on destination MAC address
  when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches usually do not need to be configured

## Slide 4: Ethernet Switching Table
Switching Table
Port Station
A1-44-D5-1F-AA-4C
B2-CD-13-5B-E4-65
C3-2D-55-3B-A9-4F
16 D4-47-55-C4-B6-9F
Ethernet Switch
UTP
UTP
UTP
UTP
A1-44-D5-1F-AA-4C
B2-CD-13-5B-E4-65
C3-2D-55-3B-A9-4F
D4-47-55-C4-B6-9F
15 C3-2D-55-3B-A9-4F
On Port 10
On Port 13
On Port 15
On Port 16
Frame
Frame

## Slide 5: Switch: traffic isolation
switch installation breaks subnet into LAN segments
switch filters packets:
  same-LAN-segment frames not usually forwarded onto other LAN segments
  segments become separate collision domains
hub
hub
hub
switch
collision domain
collision domain
collision domain

## Slide 6: Switches: dedicated access
Switch with many interfaces
Hosts have direct connection to switch
No collisions; full duplex
Switching: A-to-A’ and B-to-B’ simultaneously, no collisions
   Better performance, higher speed
switch
A
A’
B
B’
C
C’

## Slide 7: Institutional network
hub
hub
hub
switch
to external
network
router
IP subnet
mail server
web server
Broadcast domain

## Slide 8: Problems with switched LAN
Broadcast domain
  Group of network devices that will receive LAN broadcast traffic from each other
  Switches cannot break up broadcast domain
    Routers can!
Security concerns
  LANs often have confidential, mission-critical data moving across them
Performance concerns
  Broadcast traffic can degrade network performance if not properly managed
Management concerns
  Moves, adds, and changes of workstations due to reorganization

## Slide 9: Virtual LAN
Figure 13-10: Broadcast domains using VLANs
YouTube video “VLAN Concepts” https://www.youtube.com/watch?v=2hUUaG4o3DA

## Slide 10: Virtual LAN
Virtual LAN (VLAN)
  Grouping of network devices that is not restricted to a physical switch
  Frames are tagged according to LAN membership, e.g., VLAN1 (default), VLAN2, and VLAN3
  Ethernet switch establish broadcast domains according to the defined VLAN boundaries (ports are assigned to each VLAN)
Routers are used to inter-connect multiple VLANs
  On multiple interface or on a single interface
  Devices cannot communicate between VLANs without a router
  Each VLAN has its own IP subnet address

## Slide 11: Benefit of VLANs
Administrators can divide LANs logically without changing actual physical configuration
  e.g., assign a switch port to a VLAN using Cisco Network Assistant (CNA)
  https://www.youtube.com/watch?v=WMbXgtxTrBY
  This provides administrator with several benefits:
    It is easier to add and move stations on the LAN
    It is easier to reconfigure the LAN
    There is better traffic control
    There is increased security

## Slide 12: Benefit of VLANs
Figure 13-11: Securing servers with VLANs

## Slide 13: VLAN
Modern campus network architectures are tending to move away from traditional router-for-a-building design, to VLAN designs.

## Slide 14: Old Design Included a lot of Routers
routers

## Slide 15: New Design Includes VLAN Router
Switches with VLAN support
Router with VLAN support