## Slide 1: CISC 250 – Business Telecomm Networks
WAN Technologies

## Slide 2: Today’s Outline
WAN Purposes
WAN Choices
  Leased Lines
  PSDN
  DSL
  Cable Modem
  FiOS
  VPN

## Slide 3: LAN vs. WAN

## Slide 4: Wide Area Networks (WANs)
WAN Purposes
  Link sites (usually) within the same corporation
  Internet access
  Provide remote access to individuals who are off-site
1. Link Sites
3.
Remote
Access
2.
Internet
Access

## Slide 5: Wide Area Networks (WANs)
WAN Technologies
  Ordinary telephone line and telephone modem.
  Point-to-Point lines
  Public Switched Data Network (PSDN)
  Send your data over the Internet securely, using Virtual Private Network (VPN) technology
PSDN
VPN

## Slide 6: Leased Line Networks
Leased Line (Private Line or Dedicated Line)
  Point-to-point connection
  Always on
  Fixed cost depending on speed and distance
  Must be provisioned (set up). Can take weeks or months

## Slide 7: Leased Line Implementation
CSU/DSU: channel service unit/data service unit

## Slide 8: Leased Line Choices
56 kbps Leased Lines
Fractional T1 lines offer low-speed choices between 56 kbps and T1, typically:
  128 bps, 256 kbps, 384 kbps, 512 kbps, 768 kbps
T1 Leased Lines (1.544 Mbps)
T3 Leased Lines (44.736 Mbps)

## Slide 9: SONET (Synchronous Optical Networking) OC Leased Lines

## Slide 10: New Trend – DWDM
DWDM (Dense wavelength division multiplexing)
  A technology that puts data from different sources together on an optical fiber, with each signal carried on its own separate light wavelength.
Higher Speed
  (2.5 to 40 Gbps)*(16 or 32 or 128 or 160)

## Slide 11: DWDM Cost

## Slide 12: Leased Line vs. PSDN
T3 Lease
Line
Site C
Site A
Site B
OC3 Leased Line
T1 Leased
Line
T1 Leased
Line
Site E
Site D
56 kbps
Leased
Line
56 kbps
Leased
Line
56 kbps
Leased
Line
Multi-site Leased Line Mesh Network

## Slide 13: Leased Line vs. PSDN
Public Switched Data
Network (PSDN)
POP
POP
POP
POP
Site A
Site B
Point of Presence
One leased
line per site
Site D
Site C
Site E
Public Switched Data Network (PSDN)

## Slide 14: Leased Line vs. PSDN
Leased Line Network
  Many leased lines
  Individual leased line spans long distances
  Company must plan, buy switching equipment, and operate the network
Public Switched Data Network (PSDN)
  Only need one leased line from each site to a POP
  Few and short-distance leased lines
  PSDN carrier provides planning, switching, and operation of the network

## Slide 15: PSDN technologies
Frame relay with speeds from 56 kbps to 40 Mbps
Asynchronous transfer mode (ATM) with speeds from 1 to 156 Mbps.
Ethernet with speeds from 10 to 100 Gbps

## Slide 16: PSDN – Frame Relay
Designed to interconnect corporate customer LANs
  Virtual Circuits (VC): “pipe” carrying aggregate traffic between two routers
    Permanent VC (PVC)
    Switched VC (SVC)
Corporate customer leases FR service from public Frame Relay network (eg, Sprint, AT&T)

## Slide 17: Digital Subscriber Lines (DSLs)
Broadband speeds over existing telephone wire
Does not always work: distance limitations, etc.
  Usually 3 miles – attenuation and noise
  Can be fixed by repeaters
Where it does work, usually cheaper than leased lines

## Slide 18
ADSL – Asymmetric DSL
Data
WAN
PSTN
DSLAM
Splitter
Telephone
Subscriber
Premises
Telephone Company
End Office Switch
PC
Existing Telephone Wire
ADSL
Modem
downstream:
1.5 Mbps – 24 Mbps
upstream
64 kbps – 3.5 Mbps
Ordinary Telephone
Service

## Slide 19: Cable Modem Services
Delivered by cable television operator
Asymmetric, high speed
  Using Data Over Cable Service Interface Specification (DOCSIS) standard
Speed is shared by people currently downloading in a neighborhood
  Speed Test http://www.speedtest.net/

## Slide 20: Cable Modem Services
PC
Subscriber
Premises
5. Cable
Modem
4. Coaxial
Cable to
Premises
2. Optical
Fiber to
Neighborhood
3.
Neighborhood
Splitter
ISP
1. Cable
Television
Head End
6. Requires NIC or USB port

## Slide 21: FiOS: Passive Optical Network (PON) Fiber to the Home Architecture
Central Office
Typically up to 20 km (28 dB)
Passive Outside Plant
2.5 Gbps @ 1490 nm
1.2 Gbps @ 1310 nm
splitters points
Optional 1,550 nm to support local analog/digital video if required
Softswitch
(for voice)
Edge router
(data, video)
Optical
Line Terminal (OLT)
Single family homes
Multi-dwelling units
Small/medium enterprises
Optical
Network Terminal (ONT)
Source: Fiber to the Home Council
Notes: This slide was taken from a recent presentation to the FCC staff by the Fiber to the Home Council and shows the basic architecture of a Gigabit Fiber to the Premises System.
At its most basic level the Central Office uses an optical line terminal to bridge between the Internet and the passive optical distribution network, which in turn delivers service to the end users, whether they be in a multiple dwelling unit, a small or medium business, or a single family home.
The benefit of the GPON system is that no amplification of the "signals" is needed (i.e. it is passive). Active networks use amplifiers which amplify noise along with the desired signal. So the more distance a signal travels on the coax side of a HFC network, for example, the more amplifiers would be needed to get to the desired signal to the furthest point on the network and more noise would be introduced into the network.
The largest operator of GPON systems is Verizon, which has been upgrading many of its FiOS networks from the earlier generation architecture, BPON (broadband passive optical network), to GPON over the past year.

## Slide 23: Cable vs. FiOS
Cable
  Pros
    fast speed
    available in most areas
  Cons
    bandwidth shared with other users
FiOS
  Pros
    fast speed
    dedicated service (bandwidth not shared)
  Cons
    difficult to install (takes longer time)
    not available in some areas
http://broadbandnow.com/compare/Verizon-Fios-vs-Comcast-Xfinity

## Slide 24: Virtual Private Network (VPN)
A private network constructed within a public network infrastructure, such as the global internet

## Slide 25: VPN Basic Architecture
Lease an Internet connection at your speed
Connect a VPN device (router or switch) to each Internet access circuit: purpose is to create a VPN tunnel through the Internet
Sender VPN device encapsulates packet for transfer through the Internet; may encrypt for security (e.g., IPsec)
Receiver’s VPN device strips off the VPN packet and delivers the initial packet to destination; decrypt here

## Slide 27: VPN Pros & Cons
Advantages
  Low cost: mainly ISP access
  Flexibility: can get on network from anywhere
Disadvantages
  Traffic on the Internet is unpredictable
  Security is always a concern on the Internet despite encryption