## Slide 1: CISC 250 – Business Telecomm Networks
Wireless LAN – II

## Slide 2: 802.11 Security
Attackers can lurk outside your premises
  In “war driving,” drive around sniffing out unprotected wireless LANs
    http://www.wardrive.net/
    https://www.youtube.com/watch?v=w3S7yLGNjNo
    https://wigle.net/
  In “drive by hacking,” eavesdrop on conversations or mount active attacks
Site with 802.11 WLAN
Outside
Attacker

## Slide 3: 802.11 Security
There are two main components involved in securing Wireless LANs:
  Authorization/Authentication
    Open System Authentication: Service Set ID (SSID)
    MAC Address Access List
    Shared Key Authentication: WEP
    802.1x
  Encryption
    Wired Equivalent Privacy (WEP)
    Wireless Protected Access (WPA)

## Slide 4: Service Set ID (SSID)
SSID is used to identify an 802.11 network
SSID is broadcasted in Beacon Frames
  Beacon Frames are plain text
  Use of default SSID, e.g. linksys
  Turning off SSID broadcasting makes it tough to locate the network but still the hacker can sniff it from association response frames
Thus SSID is almost no defense against the experienced hacker

## Slide 5: MAC Address Access List
Wireless NIC MAC address must be included in the list for the AP to allow data to pass.
Difficult to implement on a large scale or with transient users
Lists need to be maintained in each access point, although querying a centralized list may be possible

## Slide 6: Wired Equivalent Privacy (WEP)
Original security solution offered by the IEEE 802.11 standard
Shared key between
  Stations
  An Access Point
Extended Service Set
  All Access Points will have same shared key
No key management
  Shared key entered manually into
    Stations
    Access points
  Key management a problem in large wireless LANs

## Slide 7: Wired Equivalent Privacy (WEP)
40-bit (64-bit) encryption based on the RC4 algorithm.
104-bit (128-bit) version may be vendor-specific
Keys can be entered in ASCII or Hex, depending on the manufacturer
Security Issue with WEP
  Short IV (Initialization Vector): only 24-bit
  Static key
Offers very little security at all
  https://www.youtube.com/watch?v=sJf1w7kosG8
Shared Key Authentication

## Slide 8: 802.1x Access Control
A general purpose network access control mechanism
Authentication is done with a RADIUS server, which ”tells” the access point whether access to controlled ports should be allowed or not
  AP forces the user into an unauthorized state
  user send an EAP (Extensible Authentication Protocol) start message
  AP return an EAP message requesting the user’s identity
  Identity (e.g., username and password) sent by user is then forwarded to the authentication server by AP
  Authentication server authenticate user and return an accept or reject message back to the AP
  If accept message is return, the AP changes the client’s state to authorized and normal traffic flows

## Slide 9: 802.1x Access Control

## Slide 10: WPA Overview
Wi-Fi Protected Access (WPA)
  Security standard developed after WEP’s vulnerabilities had been exposed and successfully attacked
  Development was a collaborative effort between the Wi-Fi Alliance and the Institute of Electrical and Electronics Engineers (IEEE)
  Purpose was to be an immediate solution while the long-term solution (802.11i/WPA2) was being finished

## Slide 11: WPA Overview (Cont’d)
WPA strengthened WEP by:
  Including authentication using 802.1X framework (commercial/enterprise systems) or a passphrase (home systems)
    Password length between 8 and 63 printable ASCII characters
  Creating a key hierarchy out of the master key
  Doubling the size of the initialization vector (IV) used during encryption
  Including a more robust data integrity algorithm (Michael)

## Slide 12: WPA Overview (Cont’d)
A session consists of:
  Authentication of the client to the access point (802.1X/passphrase)
  4-way handshake to exchange key values and generate the key hierarchy
  Data session to send encrypted information using the Temporal Key Integrity Protocol (TKIP)
    RC4 for encryption
    Michael for integrity checking

## Slide 13: WPA2 Overview
Wi-Fi Protected Access 2
  Security standard developed by the Wi-Fi Alliance and is an implementation of IEEE’s 802.11i
  Uses the same authentication process, 4-way handshake, and key hierarchy as WPA
  Replaces TKIP with the Advance Encryption Standard (AES) CCMP protocol
    AES in Counter-Mode for encryption
    AES in Cipher Block Chaining-Message Authentication Code (CBC-MAC) for integrity checking

## Slide 14: WPA/WPA2 Attack
Offline Dictionary Attack Overview:
  Master key is generated using:
    Passphrase and SSID
  Session keys are generated using:
    Master key, MAC address of client, MAC address of access point, nonce from client, and nonce from access point
  Attacker’s goal is to reproduce the key hierarchy to access the network
  Attacker needs to capture SSID, MAC addresses, and nonces and perform a dictionary attack to find the passphrase

## Slide 15: WPA/WPA2 Attack (Cont’d)
Tool: Kali Linux (previously BackTrack)
How to capture the 4-way handshake?
  Enter the monitoring mode
  Discover nearby networks and associated clients
    MAC addresses, WPA or WPA2, SSID
  Disassociate clients to force them to run again 4-way handshake
    Use fake disassociation control packets (not protected by IEEE 802.11i)
  Record the new 4-way handshake
    e.g., using Aireplay
  Go home and launch a dictionary attack
    Aircrack
Sample Video: https://www.youtube.com/watch?v=kpI3fQjf43E

## Slide 16: Securing against the dictionary attacks
To secure your network against these pre-computed dictionaries make sure that
  Your SSID is unique (does not appear in the existing tables)
  Your password is strong enough (sufficiently long and random :-)
    Password length between 8 and 63 printable ASCII characters
    Make it at least 13 characters!
    No dictionary words!
    the longer the better!

## Slide 17: Q & A