## Slide 1: CISC 250 – Business Telecomm Networks
Internetworking and Routing

## Slide 2: Router and Routing Decision
Router
  A special device responsible for forwarding traffic among networks
  Attached to different networks (subnets) using configurable interfaces (ports)
how does a router know where to send different packets?

## Slide 3: Routing Decision
Frame Relay Network
Routing
Table
Router E
Router G
Router H
Router F
Telephone
Connection
Incoming Packet
Token-Ring
LAN
Ethernet LAN
Router I
Destination Host
A Packet Arrives in a Port
Which Port Should the Router Send the Packet Back Out?

## Slide 4: Routing Decision
Frame Relay Network
Routing
Table
Router E
Router G
Router H
Router F
Token-Ring
LAN
Ethernet LAN
Router I
Destination Host
Destination Host May Be on One of the Attached Subnets. Router sends Packet to It
Telephone
System

## Slide 5: Routing Decision
Routing
Table
Router E
Router G
Router H
Router F
Frame Relay Network
Token-Ring
LAN
Ethernet LAN
Router I
?
?
?
?
If destination host is not on a subnet, router must select BEST next-hop router (NHR)
Telephone
System
Destination Host

## Slide 6: Routing Decision
Frame Relay Network
Routing
Table
Router E
Router G
Router H
Router F
Token-Ring
LAN
Ethernet LAN
Router I
A subnet may have multiple NHRs
Not enough to specify an interface; must also specify NHR
Telephone
System

## Slide 7: Routing Table
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2
Each Row Represents a Route to a Network or Subnet
For Each Arriving Packet, The Packet’s Destination IP Address Is Matched Against the Network/Subnet Field in Each Row

## Slide 8: Routing Table
The Interface is a port on the router
  A subnet is attached to this interface
  The subnet may have multiple hosts and next-hop routers
  NHR column specifies a specific NHR on that subnet
  For Row 4, send packet to subnet on interface 1, to NHR F
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
4
172.29.8.0
255.255.255.0 (/24)
34
F
1

## Slide 9: Routing Table
If Next-Hop Router Field says Local,
  Then the destination host is on the subnet attached to the interface (1)
  Instead of sending the packet to a next-hop router on the subnet, the router will send the packet to its destination address
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1

## Slide 10: Routing Table Examples
Windows
  cmd -> netstat –r (or “route print”)
Cisco

## Slide 11: Routing Algorithm - Find Matching Rows
For Each Packet:
First, for each row in the routing table, find matches
  Take destination IP address in packet
  Mask it with the Mask in that row
  Take the result

## Slide 12: Routing Algorithm - Find Matching Rows
For each row in the routing table find matches
  Compare the result with the Network/Subnet value in that row
  If the result matches
    Add the row to the list of matching rows for that packet
    Otherwise, ignore the row

## Slide 13: Routing Algorithm - Find Matching Rows
Destination IP Address = 172.30.33.6
Row 1
Destination IP Address = 172.30.33.6
Mask = 255.255.0.0
Result = 172.30.0.0
No match to 128.171.0.0 Network/Subnet Field Value in Row
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2

## Slide 14: Routing Algorithm - Find Matching Rows
Destination IP Address = 172.30.33.6
Row 2
Destination IP Address = 172.30.33.6
Mask = 255.255.255.0
Result = 172.30.33.0
Matches 172.30.33.0 Network/Subnet Field Value in Row
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
2
172.30.33.0
255.255.255.0 (/24)
0
Local
1
3
192.168.6.0
255.255.255.0 (/24)
12
G
2

## Slide 15: Routing Algorithm - Find Matching Rows
The default row always matches
  Mask 0.0.0.0 applied to anything results in 0.0.0.0
  This always matches the Network/Subnet value 0.0.0.0
  The router specified for this row (H) is the default router
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
15
0.0.0.0
0.0.0.0 (/0)
5
H
3

## Slide 16: Routing Algorithm - Find Matching Rows
For Each Incoming IP Packet
  Destination IP address is matched against every row in the routing table
    If the routing table has 10,000 rows, 10,000 comparisons will be made for each packet
  There can be multiple matching rows for a destination IP address, corresponding to multiple alternative routes
  After all matches are found, the best match must be selected

## Slide 17: Routing Algorithm - Find the Best Match
If only one row matches, it will be selected as the best row match
  Destination IP address = 192.168.6.7
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
3
192.168.0.0
255.255.0.0 (/16)
12
G
2

## Slide 18: Routing Algorithm - Find the Best Match
If there are multiple matches, the row with the longest length of match is selected
  Destination IP address = 128.171.17.56
  Row 7 is the longest match (24 bit match)
  Longer matches often are routes to a particular subnet within a network
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
1
128.171.0.0
255.255.0.0 (/16)
47
G
2
7
128.171.17.0
255.255.255.0 (/24)
55
H
3

## Slide 19: Routing Algorithm - Find the Best Match
If there are multiple rows with the same lengths of match, the metric column compares alternative routes
  If the metric is cost, the smallest metric wins (20)
  If the metric is speed, the largest metric wins (34)
Row
Network/
Subnet
Mask (/Prefix)*
Metric
(Cost)
Next-
Hop
Router
Interface
5
172.29.8.0
255.255.255.0 (/24)
34
F
1
8
172.29.8.0
255.255.255.0 (/24)
20
H
3

## Slide 20: Routing Algorithm - Find the Best Match
Summary
  If only one match, list row as best match
  If longest match, list row as the best match
  If tied longest length of match, select row with best metric
    May be the smallest value (say if metric is cost)
    May be the largest value (say if metric is speed)

## Slide 21: Routing Algorithm - Send the Packet Out
Finally, send the packet out a port
  Send it out from the interface in the best matching row to a host or router on the network or subnet out that port
  On that network or subnet, send packet to the
    Next-hop-router value in the best row
      or
    Destination host if next-hop router value in best row says “local”