## Slide 1: CISC 250 – Business Telecomm Networks
Network Layer Protocols
- Internet Protocol (IP)

## Slide 2: IP Address Structure
Network Part (not always 16 bits)
128.175.17.13
128.175.17.13
UD Network
The Internet
(Network ID: 128.175.0.0)
(Host ID: 0.0.17.13)
Host Part (not always 16 bits)

## Slide 3: IP Address and Network Capacities
IP address: 32-bit identifier for host, router interface
  X bits for the network part
  Y bits for the host part
# of possible networks = 2X
# of possible hosts in each network = 2Y – 2
  “all 0s” – this network
  “all 1s” – broadcasting

## Slide 4: IP Address Class Capacities
Class A:
  First bit must be 0
  7 remaining bits identify Class A network
  27 (= 128) possible class A networks
  224 – 2 (= 16777214) possible hosts in a class A network
    “all 0s” – this network
    “all 1s” – broadcasting

## Slide 5: IP Address Class Capacities
Class B:
  First two bit must be 10
  14 remaining bits identify Class B network
  214 (= 16,384) possible class B networks
  216 – 2 (= 65,534) possible hosts in a class B network
Class C:
  First three bit must be 110
  21 remaining bits identify Class C network
  221 (= 2,097,152) possible class C networks
  28 – 2 (= 254) possible hosts in a class C network

## Slide 6: “Classful” IP Address Problems
Too few network addresses for large networks
  Any network with more than 255 hosts needs a class B address
  There were only about 16,000 Class B network IDs
Network growth
  Add a new branch -> a new network of 300 hosts
  Get a new class B network license?
Solution:
  Take bits from the host number part to create a “subnet” number.

## Slide 7: Subnetting
Network Part
Subnet Part
Host Part
Total always is 32 bits.
128.175.21.15
Host 15
128.175.21.15
Lerner Subnet (21)
UD Network (128.175)
The Internet
Split the host number portion of an IP address into a subnet number and a (smaller) host number
assigned within the organization
treated as separate networks

## Slide 8: Subnet Mask
Routers and hosts use an extended network prefix (subnet mask) to identify the start of the host numbers
Subnet Mask
  1s in the network and subnet parts
  0s in the remaining bits
Subnet Mask: 255.255.255.0
Prefix length: /24

## Slide 9: With Subnetting
Hosts with same extended network address belong to the same network

## Slide 10: Mask of different classes
Class A:
255.0.0.0 or /8
Class B:
255.255.0.0 or /16
Class C:
255.255.255.0 or /24

## Slide 11: Example
Find the class of the address 128.143.137.144
  B
Given the subnet mask 255.255.255.0, what is the IP address of the subnet?
  128.143.137.0 /24

## Slide 12: Example
Find the class of the address 193.1.1.62
  C
Express it in binary format
  11000001 00000001 00000001 00111110
Given the subnet mask 255.255.255.224, what is the IP address of the subnet?
  193.1.1.32 /27
193.1.1.62: 11000001 00000001 00000001 00111110
255.255.255.224: 11111111 11111111 11111111 11100000
193.1.1.32: 11000001 00000001 00000001 00100000

## Slide 13: Possible Subnet Masks
1 1 1 1 1 1 1 1 255
1 1 1 1 1 1 1 0 254
1 1 1 1 1 1 0 0 252
1 1 1 1 1 0 0 0 248
1 1 1 1 0 0 0 0 240
1 1 1 0 0 0 0 0 224
1 1 0 0 0 0 0 0 192
1 0 0 0 0 0 0 0 128

## Slide 14: Network Planning with Subnetting
We can manipulate our subnet mask in order to create more network addresses.
Example:
  We were given a Class C license (206.15.143.0) from our ISP for our network
    This gives us 1 Network (206.15.143.0) with the potential for 254 host addresses (206.15.143.1 to 206.15.143.254).
  But we have a LAN made up of 5 sub-networks with the largest one serving 25 hosts.
    So we need to Subnet...

## Slide 15: Network Planning with Subnetting
We need at least 5 subnets
  23 will give us 8 subnet addresses
We need at least 25 hosts per network
  25-2 will give us 30 hosts per subnet
This will work!
  steal the first 3 bits from the host’s portion of the address to give to the subnet portion
    extended-network-prefix is /27
  still have 5 (8-3) left for the host portion

## Slide 16: Network Planning with Subnetting
0 0 0 0 0 0 0 0 0
0 0 1 0 0 0 0 0 32
0 1 0 0 0 0 0 0 64
0 1 1 0 0 0 0 0 96
1 0 0 0 0 0 0 0 128
1 0 1 0 0 0 0 0 160
1 1 0 0 0 0 0 0 192
1 1 1 0 0 0 0 0 224
To get the address for each subnet:
Check the original host portion (last 8 bits of the IP address)
For Subnet
For Host

## Slide 17: Network Planning with Subnetting
Subnet #1: 206.15.143.0
Subnet #2: 206.15.143.32
Subnet #3: 206.15.143.64
Subnet #4: 206.15.143.96
Subnet #5: 206.15.143.128
Subnet #6: 206.15.143.160
Subnet #7: 206.15.143.192
Subnet #8: 206.15.143.224
Addresses for all subnets:

## Slide 18: Subnetting Exercise
Assume that you have been assigned the 200.35.1.0/24 network block. Define an extended-network-prefix that allows the creation of 40 hosts on each subnet.
  A minimum of six bits are required to define 40 hosts so the extended-network-prefix is /26 (26 = 32 -6)

## Slide 19: Subnetting Exercise
What is the maximum number of hosts that can be assigned to each subnet?
  The maximum number of hosts on each subnet is 26 - 2, or 62
What is the maximum number of subnets that can be defined?
  The maximum number of subnets is 22, or 4.

## Slide 20: Subnetting Exercise
Specify the subnets of 200.35.1.0/24 in binary format and dotted decimal notation.
Subnet #0: 11001000.00100011.00000001. 00000000 = 200.35.1.0 /26
Subnet #1: 11001000.00100011.00000001. 01000000 = 200.35.1.64 /26
Subnet #2: 11001000.00100011.00000001. 10000000 = 200.35.1.128 /26
Subnet #3: 11001000.00100011.00000001. 11000000 = 200.35.1.192 /26

## Slide 21: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  network portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23

## Slide 22: CIDR
Efficient Allocation of Addresses
  Subnetting: division of networks into smaller units
  Supernetting: combination of smaller networks into larger ones
    E.g. allows the aggregation of contiguous blocks of Class-C addresses into larger networks
CIDR-capable routers explicitly store the network masks (prefix length) in the router