## Slide 1: CISC 250 – Business Telecomm Networks
Network Architecture
– A Layered Model
Dr. Jinwei Cao
Dept. of ACCT & MIS
University of Delaware

## Slide 2: Today’s Outline
Needs For A Layered Model
Protocols and Network Architecture
Standards
  OSI
  TCP/IP
  Hybrid

## Slide 3: You have a gift …
You need to send it to ______ …

## Slide 4
You
_____

## Slide 5: A Layered Model
Task broken into subtasks
  Implemented separately in layers in stack
Each layer provides a service to the layer above
Each layer hides details of how the service is provided from the layer above
Functions needed in both systems
The Nth layer on one machine “talks to” or interacts with the Nth layer on another machine

## Slide 6: Protocols
Conventions and rules governing this interaction are specified by the Layer N Protocol
  A protocol is an agreement about how communications are to proceed
  Without a protocol communication can be difficult or even impossible
  E.g. Telephone conversation, Postal addresses

## Slide 7: Division of Protocols
Connection-Oriented
  a logical connection be established between two devices before transferring data
  a circuit is not a prerequisite for a connection
  Circuit-switched => connection-oriented, but not all connection-oriented => circuit switching
Connectionless
  do not establish a connection between devices

## Slide 8: Circuit Switching

## Slide 9: Packet Switching
Original Message
Computer X
Packet
Switch
A
Packet
Switching
Decision
B
C
Computer Y
F
E
D
1. Break message into
Smaller packets
(or frames)
2. Route packets individually;
Packet switches along the way
Make decisions about the packet

## Slide 10: Packetizing
Packets (also known as):
  Cells, frames, packets, block, data units
  However, they are loosely used interchangeably!
    Cell: is a 53-bytes packet used by ATM
    Frame: is used in the data link layer
    Packet: is used in the network layer
  Examples:
    Ethernet frame, Token ring frame
    ATM cell

## Slide 11: Encapsulation
Addition of Control Information to Data
  Address Information
  Error-detecting Code
  Protocol Control
N-layer PDU (Protocol Data Unit) = Header + (N+1)-layer PDU + Trailer

## Slide 12: Network Architecture
The set of protocols and layers together make up the Network Architecture
  A Network Architecture Specification must provide enough information to allow implementation in hardware/software
  Implementation specific details are not part of the architecture and should be irrelevant for inter-operation
  With one protocol per layer we have a Protocol Stack

## Slide 13: Standardized Network Architectures
Required for devices to communicate
Vendors have more marketable products
Customers can insist on standards based equipment
Two standards:
  OSI Reference model
    Never lived up to early promises
  TCP/IP protocol suite
    Most widely used
    De facto

## Slide 14: OSI Model
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven Layers
A Theoretical System Delivered Too Late!
TCP/IP Is the De Facto Standard

## Slide 15: OSI Model

## Slide 16: OSI Layers
Application -------- Acronyms
Presentation ------ Pointless
Session ------------ Students
Transport ---------- Teach
Network ------------ Not
Data Link ----------- Do
Physical ------------- Please

## Slide 17: OSI Layers (1)
Physical
  Physical Interface Between Devices
    Mechanical – hardware, topology
    Electrical - signaling
Data Link
  Activating, Maintaining and Deactivating a Reliable Link – between local devices
  Media access control
  Error Detection and Control
    Higher Layers May Assume Error Free Transmission

## Slide 18: OSI Layers (2)
Network
  Delivery of Information
    logical addressing
    routing
  Fragmentation and assembly
  Error handling
  Not Needed on Direct Links
Transport
  Reliability control between End Systems (hosts, computers)
    In Sequence
    In good flow
    Error Free
    No Losses
    No Duplicates

## Slide 19: OSI Layers (3)
Session
  Control of Dialogues Between Processes
    Establish, manage, and terminate dialogues
Presentation
  Data Formats and Coding
  Data Compression
  Encryption
Application
  Implement user required functionalities
    Send letters, move files

## Slide 20: The OSI Environment
Video Demo

## Slide 21: TCP/IP Model
TCP = Transmission Control Protocol
IP = Internet Protocol
TCP/IP is an Internet Model
This model has only 4-layers
It is simpler and more practical than the 7-layered OSI-Model
Created by the US Dept of Defense (DoD)

## Slide 22: Father(s) of TCP/IP
Vint Cerf
Bob Khan

## Slide 23: TCP/IP Model
Application Layer:
  Combines all the application-related issues into 1-layer
  Includes the Sessions/Presentation layers
Transport Layer:
  Deals with the QoS and other issues like:
    Reliability, flow control and error correction
Internet Layer:
  Delivery
  Routing
Network Interface Layer:
  Ensures the physical links

## Slide 24: TCP/IP, OSI, and TCP/IP-OSI Hybrid Architecture
Presentation
TCP/IP
OSI
Hybrid TCP/IP-OSI
Application
Application
Application
Session
Transport
Internet
Transport
Network
Transport
Internet
Data Link
Physical
Data Link
Physical
Network Interface

## Slide 25: Message Communication in Hybrid TCP/IP-OSI
Application
Layer
HTTP Msg
Application
Layer
Transport
Layer
TCP Seg
Transport
Layer
Internet
Layer
IP Packet
Internet
Layer
Internet
Layer
Client PC
Server
Ethernet Switch
Router
Data Link
Layer
Ethernet
Frame
Data Link
Layer
Data Link
Layer
Data Link
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer

## Slide 26: Layer Design Issues
Most layers need:
  Message segmentation and aggregation
  Some form of Addressing to identify senders and receivers of messages
  Multiplexing/Demultiplexing of multiple message streams to optimize channels
  Flow control (fast sender vs. slow receiver)
  Error controls (detection and correction)
  A set of rules for data exchange
  Routing of messages when there may be several physical paths

## Slide 27: A protocol for
The class?
Your team communication?