## Slide 1: CISC 250 – Business Telecomm Networks
Lab 1
- Introduction to Wireshark

## Slide 2: Recap - Encapsulation

## Slide 3: Message Communication in Hybrid TCP/IP-OSI
Application
Layer
HTTP Msg
Application
Layer
Transport
Layer
TCP Seg
Transport
Layer
Internet
Layer
IP Packet
Internet
Layer
Internet
Layer
Client PC
Server
Ethernet Switch
Router
Data Link
Layer
Ethernet
Frame
Data Link
Layer
Data Link
Layer
Data Link
Layer
Physical
Layer
Physical
Layer
Physical
Layer
Physical
Layer

## Slide 4: Recap - HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language:fr
(extra carriage return, line feed)
request line
(GET, POST,
HEAD commands)
header
lines
Carriage return,
line feed
indicates end
of message

## Slide 5: Recap - HTTP response message
HTTP/1.1 200 OK
Connection close
Date: Thu, 06 Aug 1998 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 1998 …...
Content-Length: 6821
Content-Type: text/html
data data data data data ...
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
HTML file

## Slide 6: Packet Sniffing
Currently Data just travels around your network like a train. With a packet sniffer, get the ability to capture the data and look inside the packets to see what is actually moving long the tracks.

## Slide 7: Packet Sniffing
Sometimes referred to as Network Monitoring Tools
Can be used legitimately by network and system administrators to verify network traffic and diagnose problems
Can be used to determine what systems and protocols are unprotected/unencrypted in a network and take action (good/bad)
Can be used to obtain critical information (passwords, cc numbers; anything unencrypted that is transmitted over the network) by malicious hackers

## Slide 8: Packet Sniffing : Tools
Wireshark (http://www.wireshark.org/)
  King of the Packet Analyzers!
    Available for Linux, Unix, Windows
  Requires WinPcap for Captures
tcpdump
  The original packet sniffer
  Ships by default with many versions of linux
Many more . . .

## Slide 9: Wireshark Application

## Slide 10: Display Filter
Note the box at the top of Wireshark for display filters
Select only some of the packets captured for display
The comparison operators can be expressed either through C-like symbols, or through English-like abbreviations:
  eq, == Equal
  ne, != Not equal
  gt, > Greater than
  lt, < Less Than
  ge, >= Greater than or Equal to
  le, <= Less than or Equal to

## Slide 11: Advanced Filtering
Filter for just that stream
(ip.addr eq 207.46.133.140 and ip.addr eq 172.17.22.56) and
(tcp.port eq 21 and tcp.port eq 3511)
Filter for traffic between two hosts
ip.addr == 207.46.133.140 and ip.addr == 172.17.22.56
Filter for IP Traffic and removal of other traffic
ip and !(nbns) and !(msnms) and !(browser) and !(rip)

## Slide 12: Capture Filters
The capture filter syntax follows the rules of the pcap library
This syntax is different from the display filter syntax.
Sample filters
  src ip 192.168.1.1
  ether src 00:50:BA:48:B5:EF

## Slide 13: More On Capture Filters
A capture filter for HTTP that captures traffic to and from a particular host
  tcp port 80 and host 10.10.10.5
A capture filter for HTTP that captures traffic not from a particular host
  tcp port 80 and not host 10.10.10.5
A capture filter to and from an ethernet address
  ether 00:00:01:01:02:22

## Slide 14: Lab 1
Test Run: http://gaia.cs.umass.edu/wireshark-labs/INTRO-wireshark-file1.html
Basic HTTP request/response http://gaia.cs.umass.edu/wireshark-labs/HTTP-wireshark-file1.html
HTML with Embedded Objects http://gaia.cs.umass.edu/wireshark-labs/HTTP-wireshark-file4.html
HTTP to TCP http://gaia.cs.umass.edu/wireshark-labs/HTTP-wireshark-file3.html
HTTP CONDITIONAL GET/response http://gaia.cs.umass.edu/wireshark-labs/HTTP-wireshark-file2.html

## Slide 15: Downloading a Complex Webpage with Two Graphics Files
HTML Document
Client PC
Browser
Webserver
Application
Webserver
Download Requires 3
HTTP Request-Response Cycles;
Downloads HTML Page First
It has Tags to Identify Other Files
As
Displayed
2
Graphics
Files
HTML Document

## Slide 16: Downloading a Complex Webpage with Two Graphics Files
Client PC
Browser
Webserver
Application
Webserver
Based on Tags in HTML Document,
Browser Requests Downloads of
Remaining Graphics or Other Files
Browser Renders Combined Webpage on Screen
As
Displayed
2
Graphics
Files