## Slide 1: CISC 250 – Business Telecomm Networks
Transport Layer Protocols – TCP and UDP

## Slide 2: Today’s Outline
Sockets and Port Number
Transport Layer Protocols
  Transmission Control Protocol (TCP)
    TCP Segment Format
    TCP Connection Management
    TCP Flow Control
  User Datagram Protocol (UDP)
  TCP vs. UDP

## Slide 3: Sockets
Application process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door which brings message to socket at receiving process
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
controlled
by OS
controlled by
app developer
API: (1) choice of transport protocol; (2) ability to fix a few parameters

## Slide 4: Addressing processes
identifier of a process includes both IP addresses and port numbers associated with the process on hosts.
Example port numbers:
  HTTP server: 80
  Mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  Port number: 80

## Slide 5: Use of Port Numbers - I
Well-known port numbers are 0 to 1023. These are used by popular applications.
  Servers/daemons usually use well-known ports
    Any client can identify the server/service
Registered port numbers (1024 to 49152)
  used for less central applications.
http://www.iana.org/assignments/port-numbers
Ephemeral port numbers: 49153 to 65535
  Clients usually use dynamic ports
    Assigned by the client kernel at run time
  Traditionally (including Windows systems) take the range of 1024 through 4999
Notes: FTP: 21
telnet: 23
DNS: 53

## Slide 6: Use of Port Numbers - II
From 172.171.18.22:50247
To: 172.168.17.13:80
Client PC
172.171.18.22
Webserver
172.168.17.13
Port 80
SMTP Server
172.30.17.13
Port 25
From Ephemeral
Port 50247
To Well-Known
Port 80
Socket =
IP Address:Port Number

## Slide 7: Use of Port Numbers - III
From: 172.168.17.13:80
To: 128.171.18.22:50247
Client PC
172.171.18.22
Webserver
172.168.17.13
Port 80
SMTP Server
172.30.17.13
Port 25
From 172.171.18.22:50247
To: 172.168.17.13:80

## Slide 8: Use of Port Numbers - V
From 172.171.18.22:50247
To: 172.168.17.13:80
From: 172.171.18.22:49345
To: 172.30.17.13:25
Client PC
172.171.18.22
Webserver
172.168.17.13
Port 80
SMTP Server
172.30.17.13
Port 25
From Ephemeral
Port 50247
To Well-Known
Port 80
From Ephemeral
Port 49345
Different ephemeral port numbers for different TCP connections

## Slide 9: Transport Layer Protocols
provide logical communication between application processes running on different hosts
transport protocols run in end systems
  sender side: breaks app messages into segments, passes to network layer
  receiver side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 10
Transport Layer Protocols
Transmission Control Protocol (TCP)
  Connection-oriented; reliable, in-order delivery
    Reliable data transfer
    Flow control
    Congestion control
User Datagram Protocol (UDP)
  Connectionless – unreliable, unordered delivery

## Slide 11: TCP: Overview
connection-oriented:
  handshaking (exchange of control msgs) before data exchange
flow controlled:
  sender will not overwhelm receiver
    set window size
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
send & receive buffers

## Slide 12: User Datagram Protocol (UDP)
PC
Transport Process
Webserver
Transport Process
UDP Datagram
Close
(4)
Connectionless and Unreliable
Places a Lighter Load on the Network than TCP
Useful Where the Loss of an Occasional
Application Message is Not a Serious Problem
As in Regular Network Status Messages
Or Where There is No Time for Retransmission,
As in Voice Transmission

## Slide 13: TCP Versus UDP
TCP
UDP
Layer
Message name
Processing power
required
Reliability
Connections?
Transport
Transport
TCP segment
UDP datagram
Reliable
Unreliable
Connection-oriented
Connectionless
Heavyweight
Lightweight

## Slide 14: TCP Segment
Source Port Number (16 bits)
Destination Port Number (16 bits)
Sequence Number (32 bits)
Acknowledgment Number (32 bits)
Window Size
(16 bits)
Header Length
(4 bits)
Reserved
(6 bits)
Flag Fields
(6 bits)
Options (if any)
TCP Checksum (16 bits)
Urgent Pointer (16 bits)
Padding
Data Field
Bit 0
Bit 31
Flag fields are one-bit fields. They include SYN, ACK, FIN and RST.

## Slide 15: Sequence Numbers
32 bit sequence numbers
TCP breaks byte stream from application into segments (limited by Max. Segment Size)
Each segment has a sequence number
  Initial number selected at connection time
  Subsequent numbers indicate first data byte number in segment

## Slide 16: Acknowledgements (ACK)
ACK# indicates next data byte expected
  Next sequence # from the other side
Used for Error Control
  Each correct TCP segment is acknowledged, except for pure acknowledgements and resets
  Sender listens to be sure that each TCP segment is acknowledged
  If a segment is not acknowledged in a reasonable period of time, the sender resends it

## Slide 17: TCP Connection Management - Establishing Logical Connection
Two blue armies, need to attack simultaneously
  How to make sure the two sides are on the same page?
    messages are delivered reliably?
Notes: Two blue armies are each poised on opposite hills preparing to attack a single red army in the valley. The red army can defeat either of the blue armies separately but will fail to defeat both blue armies if they attack simultaneously. The blue armies communicate via an unreliable communications system (a foot soldier). The commander with one of the blue armies would like to attack at noon. His problem is this: if he sends a message to the other blue army, ordering the attack, he cannot be sure it will get through. He could ask for acknowledgement, but that might not get through. Is there a protocol that the two blue armies can use to avoid defeat?
No. There is no way to be assured that the last message gets through, except by acknowledging it. Thus, either the acknowledgment process continues forever, or one army has to send the last message and then act with uncertainty.

## Slide 18: 3-Way Handshake
PC
Transport Process
Webserver
Transport Process
1. SYN (SEQ# = x)
2. SYN, ACK (SEQ# = y, ACK# = x+1)
3. ACK (ACK# = y+1)
Open

## Slide 19: Data Transfer
PC
Transport Process
Webserver
Transport Process
4. Data = HTTP Request (part 1: 100 bytes)
(SEQ# = x+1, ACK# = y+1)
5. ACK (SEQ# = y+1, ACK# = x+1+100)
6. Data = HTTP Request (part 2: 200 bytes)
(SEQ# = x+1+100, ACK# = y+1)
7. ACK (SEQ# = y+1, ACK# = x+1+100+200)
Carry
HTTP
Request &
Response
After Opening, Data are Transferred

## Slide 20: Data Transfer
PC
Transport Process
Webserver
Transport Process
8. Data = HTTP Request (part 3: 300 bytes)
(SEQ# = x+1+100+200, ACK# = y+1)
9. ACK (SEQ# = y+1, ACK# = x+1+100+200+300)
10. Data = HTTP Response (200 bytes)
(SEQ# = y+1, ACK# = x+1+100+200+300)
11. ACK (SEQ# = x+1+100+200+300, ACK# = y+1+200)
Carry
HTTP
Request &
Response
After Opening, Data are Transferred

## Slide 21: 4-Way Close
PC
Transport Process
Webserver
Transport Process
12. FIN (Close)
13. ACK
14. FIN
15. ACK
Close

## Slide 22: Abrupt Close
PC
Transport Process
Webserver
Transport Process
8. RST (Close)
Close
Reset
Abrupt Close
No Acknowledgement
Usually When There is an Error Condition

## Slide 23: TCP Flow Control
Flow Control
  One TCP process transmits too fast
  Other TCP process is overwhelmed
  Receiver must control transmission rate
  This is flow control
TCP Process
TCP Process
Too Much
Data
Flow Control Message

## Slide 24: TCP Flow Control
A TCP segment has a Window Size field
  Tell how many more bytes the sender can send beyond the segment being acknowledged
TCP Process
TCP Process
Data
Acknowledgement with Window Size Field

## Slide 25: TCP Flow Control
Example
  TCP segment contained bytes 45-89
  Acknowledgement number for TCP segment acknowledging the segment is 90
  If Window Size field value is 50, then
  Sender may send through byte 140
  Must then stop unless the window has been extended in another acknowledgement

## Slide 26: TCP Flow Control
Each Acknowledgement extends the window of bytes that may be sent
  Called a sliding window protocol
1-44
45-79
80-419
400
May send through 480
1-44
45-79
80-419
420-630
500
May send through 920