## Slide 1: CISC 250 – Business Telecomm Networks
Networking Fundamentals
Dr. Jinwei Cao
Dept. of ACCT & MIS
University of Delaware

## Slide 2: Today’s Outline
Network & Internet
Network Performance Metrics
Network Structural Models
Protocols

## Slide 3: Network
Application
Application
Client
Station
Server
Station
Warriors of the Net

## Slide 4: The Internet
A Network of Networks
Interconnected by Routers
Network X
Network Z
Network Y
Switches
Routers
Switches
How Does the Internet Work?

## Slide 5: Internet: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, Level 3, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)
http://www.internetexchangemap.com/

## Slide 6: Tier-1 ISP: e.g., Sprint
Sprint US backbone network
Seattle
Atlanta
Chicago
Roachdale
Stockton
San Jose
Anaheim
Fort Worth
Orlando
Kansas City
Cheyenne
New York
Pennsauken
Relay
Wash. DC
Tacoma
DS3 (45 Mbps)
OC3 (155 Mbps)
OC12 (622 Mbps)
OC48 (2.4 Gbps)
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence

## Slide 9: Level 3 Backbone

## Slide 10: Internet: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs (e.g., Comcast)
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 11: Internet: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 12: Internet: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 13
Partial map of the Internet based on the January 15, 2005 data found on opte.org. Each line is drawn between two nodes, representing two IP addresses. The length of the lines are indicative of the delay between those two nodes. This graph represents less than 30% of the Class C networks reachable by the data collection program in early 2005. Lines are color-coded according to their corresponding RFC 1918 allocation as follows:
  Dark blue: net, ca, us
  Green: com, org
  Red: mil, gov, edu
  Yellow: jp, cn, tw, au, de
  Magenta: uk, it, pl, fr
  Gold: br, kr, nl
  White: unknown

## Slide 14: Netflix’s USA ISP Speed Index

## Slide 15: The Future?
Click the links to watch videos
The Fight for the Open Internet
  What is “Net Neutrality”?
  Comcast, Level 3, and Netflix
  PRISM & Xkeyscore
  WikiLeaks
The Internet of Things

## Slide 16: Network Performance Metrics
Bandwidth (capacity) / Throughput (actual)
  data transmitted per time unit
  Notation: bps = bits per second
  Network speed test
Latency (delay)
  time to send message from point A to point B
  one-way versus round-trip time (RTT)
  Latency = Propagation + Transmit + Queue
    Propagation = Distance / propagation speed in medium (~2x108 m/sec)
    Transmit = Size / Bandwidth
  Demo

## Slide 17: Network Performance Metrics
Availability
  Percent of time the network is available to users for transmission and reception
  Want 24x7x365 availability
  Telephone network: Five 9s (99.999%)
Error Rate
  Percent of lost or damaged messages or bits

## Slide 18: Network Structural Models
Client/Server
Peer-to-Peer

## Slide 19: Thin clients and Cloud Computing
The thin client has a limited processing power, memory or storage
Applications run on the web, in a “cloud” (see this video!)
Amazon offers basic services: storage, basic computing elements
Google offers more advanced services: word processors, spreadsheets, etc..
IBM offers Blue Cloud
Thin
Client
Application
Cloud
OS
Storage
Desktop

## Slide 20: Protocols
A protocol is an agreement about how communications are to proceed
Without a protocol communication can be difficult or even impossible
E.g. Telephone conversation, Postal addresses

## Slide 21: Division of Protocols
Connection-Oriented
  a logical connection be established between two devices before transferring data
  a circuit is not a prerequisite for a connection
  Circuit-switched => connection-oriented, but not all connection-oriented => circuit switching
Connectionless
  do not establish a connection between devices

## Slide 22: Packet Switching
Original Message
Computer X
Packet
Switch
A
Packet
Switching
Decision
B
C
Computer Y
F
E
D
1. Break message into
Smaller packets
(or frames)
2. Route packets individually;
Packet switches along the way
Make decisions about the packet

## Slide 23: Circuit Switching